M-AUDIO KEYSTATION61 MK3 Key Scan
		CN13					CN14
		1	2	3	4	5	6	7	8	9	10	11	12	13	1	2	3	4	5	6	7	8	9	10	11	12
		PB / 9	PB / 8	PB / 5	PB / 4	PB / 3	PA / 15	NC	PA / 10	PA / 9	PA / 8	PB / 15	PB14	PB13	PC14	PC15	PA0	PA1	PA2	PA3	PA4	PA5	PA6	PA7	PB0	PB1
1	C2				0			NC					1	2
2	C♯			0					1	2
3	D		0					1	2
4	D♯	0					1	2
5	E					1	2				0
6	F					1	2			0
7	F♯					1	2		0
8	G					1	2	0
9	G♯				0					1	2
10	A			0					1	2
11	A♯		0					1	2
12	B	0					1	2
13	C3					1	2					0
14	C♯					1	2					0
15	D					1	2				0
16	D♯					1	2			0
17	E				0				1	2
18	F			0					1	2
19	F♯		0					1	2
20	G	0					1	2
21	G♯					1	2					0
22	A					1	2					0
23	A♯					1	2					0
24	B					1	2					0
25	C4				0	1	2
26	C♯			0		1	2
27	D		0			1	2
28	D♯	0				1	2
29	E					1	2					0
30	F					1	2					0
31	F♯					1	2					0
32	G					1	2					0
33	G♯				0					1	2
34	A			0					1	2
35	A♯		0					1	2
36	B	0					1	2
37	C5					NC					0					1	2
		1	2	3	4	5	6	7	8	9	10	11	12	13	1	2	3	4	5	6	7	8	9	10	11	12
		1	2	3	4	5	6	7	8	9	10	11	12	13	1	2	3	4	5	6	7	8	9	10	11	12
		PB / 9	PB / 8	PB / 5	PB / 4	PB / 3	PA / 15		PA / 10	PA / 9	PA / 8	PB / 15	PB14	PB13	PC14	PC15	PA0	PA1	PA2	PA3	PA4	PA5	PA6	PA7	PB0	PB1
38	C♯					NC					0					1	2
39	D					0					1	2
40	D♯					0					1	2
41	E				0					1	2
42	F			0					1	2
43	F♯		0					1	2
44	G	0					1	2
45	G♯					0					1	2
46	A					0					1	2
47	A♯					0					1	2
48	B					0					1	2
49	C6				0					1	2
50	C♯			0					1	2
51	D		0					1	2
52	D♯	0					1	2
53	E					0			1	2
54	F					0				1	2
55	F♯					0					1	2
56	G					0					1	2
57	G♯				0					1	2
58	A			0					1	2
59	A♯		0					1	2
60	B	0					1	2
61	C7					NC					0	1	2
62	!					o!		1	2
63	!					o!			1	2
64	!					o!				1	2

Key:
0 – Output	A 4us 4V pulse repeated at 100us intervals
1 – Input	The first contact to operate.
2 – Input	The second contact to operate
! _ Spare	Add a diode and contact to generate codes in these unused positions
Notes on use with Midi Interface:
a. Scanned outputs are connected to scanned inputs via dual diodes in a package marked A1, probably BAW56. Each piano key operates two contacts. The table above shows contact 1 which closes before contact 2 as the piano key is depressed. Contact 2 releases before contact 1 as the piano key is released.
b. CN13 pin 7 has no connection.
c. CN13 and CN14 are 2mm pitch of unknown type, with 2mm pitch ribbon cable but may be mated with 2mm pitch pin headers.
d. A peddleboard using the same scanning formation leaves some GPIO available e.g.PA1-PB1 become available for 8 analogue expression inputs, PB3-PB14 available for additional contacts.